## Slide 1
Joel Bursztyn
May
. 2014
Embedded SW Oven Challenge

## Slide 2: Exercise - Oven Solution KingsToaster.txt
Oven Controller
Oven has the following data
  Temperature (0.. 400)
  Heat: ambient, hot, over Heat
  Humidity:
    low, mid-low, mid high, high, too High
  User – immediate stop request
  Off/On button
  Turbo Fan on
  Electric consumption
    Low, Medium, High, Too-High
  Time from Start, Time to finish
  Heat command
    Overide anything except Emergency (heat/consumption)
User Program:
  Time & required temperature
Controls:
  Heater, Fan, heat on Led, Humidity status,
  Emergency LED.
Controls in the next slides
To Do
Design the SOC to maintain such a Appliance
Write the logic for that oven
KISS and Efficient(where needed)
Generate events (Random and explicit) that test this logic.
Input & Output
User Program generate and print events
Print reaction of the logic to the events
Oven Required special Behavior
On Emergency (any red situation ) stop!
On High Humidity or delta temp>100 start fan
On Delta temp> 10 [dis]operate heater

## Slide 3: The Oven
Required Temp
Time
Stop Immediately
Heat Immediately
On/Off
Heat Led On
Turbo Fan
Humidity Status
Emergency-Status
Heater

## Slide 4: Oven Control
HeaterOn(R/W)
FanOn(R/W)
HeatLedOn (R/W)
Humidity LedOn(R/W)
Stop Immediately(W)
PowerOn
Over Heat
Over Humidity
Over Current Consumption
Reset
Future Use
Future Use
Control and Status &1000550
9 8 7 6 5 4 3 2 1 0
Resolution (bit) | Range | Address | Device
Seconds | 0-3600*36 | 1000554 | Time (R/W)
2 Celsius Degrees | -25- 400 | 1000558 | Heat (R/W)
1 Amper | 0-15 Amper | 4:100055C | Electric Consumption
Low-TooHigh | 0-7 | 3:100055C | Humidity

## Slide 5: Oven Challenge
Draw the System Architecture (Hardware)
Draw the SW Architecture Logic view
  Identify all the capabilities blocks
  Define system State Machine
CPU